## Slide 1
MACHINE ELEMENTS 2 | FINAL PRESENTATION
WOODCHIPPER DESIGN
A comprehensive design analysis focusing on structural integrity, power transmission, and ISO standard component selection.

## Slide 2
PRESENTATION STRUCTURE
PROJECT SCOPE
Engineer a robust, mobile woodchipper driven by a 7.5 kW electric motor to process 50mm branch diameter.
Part I: Material Selection & Core Assembly
Part II: Power Unit Specification
Part III: Standard Machine Elements
Part IV: Engineering Calculations
Part V: System Integration
➤
➤
➤
➤
➤
AGENDA & OBJECTIVES

## Slide 3
CORE ASSEMBLIES
Design specifications based on high-inertia loads.
CUTTER ASSEMBLY
Disc: Ø400 mm | AISI 4140. Selected for flywheel effect (Inertia).
Main Shaft: Ø35 mm | C45 Steel. Standard carbon steel for machinability.
Knives: D2 Tool Steel. 58-60 HRC for edge retention.

## Slide 4: STRUCTURAL FRAME
Feeder: Alu 6061-T6. Lightweight intake.
Chassis: ASTM A36. Weldable structural steel.

## Slide 5
SEVA-TEC MX3-132S2-2
This high-efficiency IE3 motor serves as the primary driver.
Parameter | Specification
Rated Power | 7.50 kW
Speed | 2920 RPM
Weight | 53.8 kg
Mounting | IM B5 (Flange)
POWER UNIT SPECIFICATION

## Slide 6
DESIGN CONSTRAINTS
Manufacturer datasheets imposed specific geometric constraints on the drivetrain.
Shaft Diameter: 38 mm Dictated the use of a 38mm Taper Lock Bushing.
Mounting Holes: 15 mm Selection of M15 fasteners (Fine Pitch).
➤
➤
INTERFACE DIMENSIONS

## Slide 7
UCF 207 FLANGE UNIT
Standard ISO 4-bolt flange units were selected to support the Ø35mm main shaft.
Spec | Value
Standard | ISO 3228
Bore | 35 mm
Housing | Cast Iron (HT200)
Feature | Self-Aligning Insert
ROTOR SUPPORT

## Slide 8
V-BELT DRIVE (ISO 4184)
A multi-belt drive system designed for shock absorption and torque transfer.
Belt Profile: SPZ Section (Metric Wedge)
Configuration: 3 Parallel Belts
Pulleys: ISO 4183 Deep Groove
Tensioner: Manual Slotted Bracket
➤
➤
➤
➤
POWER TRANSMISSION

## Slide 9: TENSIONER
Manually Adjustable Pivoting Idler Tensioner
Consisting of tensioner arm, tensioner pulley and a pivot bolt.

## Slide 10: MOBILITY
300mm pair of wheels and handle bars were used

## Slide 11
NON-STANDARD SOLUTIONS
Fine pitch high-tensile fasteners were required to match component constraints.
Application | ISO Std | Designation
Motor Mount | ISO 8676 | M15 x 1.5 (10.9)
Tensioner | ISO 8676 | M11 x 1.0 (10.9)
Locking | ISO 10512 | Nyloc Nut (10)
FASTENER SELECTION

## Slide 12
FINAL ASSEMBLY

## Slide 13
Thank you for your attention.